## Slide 1
Where the gains came from
The feedforward terms, fitted
Kff ≈ 38 PWM per rad/s and Kstat ≈ 8 PWM, both fit from three independent bench campaigns, wheels free, no load. The static term exists because a straight line through the origin cannot reproduce breakaway friction.
The PID terms, computed then checked
Ki = 250 from direct synthesis on the fitted plant gain, not tuned by hand. Kp = 45 and Kd = 0.5 were re-derived from a later, measured plant time constant, then verified by sweeping the recomputed values against the shipped ones on real hardware — the original gains won and were kept.
THE NARROW AISLE ROBOT
Annual Progress Seminar · Aritra Das · 25D0074 · IIT Bombay
Notes: Five gains, two families. Kff and Kstat came from fitting three bench campaigns to a two-term friction model. Ki came from direct synthesis, computed once from the fitted plant gain and a chosen closed-loop time constant, not searched. Kp and Kd were both re-derived after a later bench test finally measured the plant time constant directly, at half the value that had been assumed; the recomputed gains were swept against the shipped ones on real hardware and lost on overshoot, so the original values were kept, confirmed rather than changed.